## PCB Editor Shortcuts
SHIFT + R	Cycle through three routing modes (ignore, avoid or push obstacle)
SHIFT + E	Toggle electrical grid on/off
SHIFT + B	Build Query
SHIFT + PAGE UP	Zoom-in in small increments
SHIFT + PAGE DOWN	Zoom-out in small increments
CTRL + PAGE UP	Zoom-in to 400%
CTRL + PAGE DOWN	Fit document into view
CTRL + END	Jump to defined relative origin for the workspace
ALT + END	Redraw current layer only
ALT + INSERT	Paste on current layer
CTRL + G	Pop up Snap Grid dialog
G	Pop up Snap Grid menu
N	Hide the ratsnest while moving a component
L	Flip component being moved to other side of board
SHIFT + F1	Pressed while routing, displays the appropriate interactive routing shortcut keys
TAB	Pressed while routing, length tuning, component or string placement displays appropriate interactive editing dialog
F2	Display Board Insight and Heads Up display options
CTRL + Left-click	Highlight routed net under cursor (repeat in free space to clear)
CTRL + SPACEBAR	Cycle through connection lines modes during interactive routing
BACKSPACE	Remove last track corner during interactive routing
SHIFT + S	Toggle single layer mode on/off (or cycle through Single Layer Modes set in PCB Preferences: Board Insight Display)
O, D, D, O, ENTER	Set all primitives to display in draft mode
O, D, F, O, ENTER	Set all primitives to display in final mode
O, D (or CTRL + D)	Access Show/Hide page of View Configurations dialog
L	Access Board Layers And Colors page of View Configurations dialog
CTRL + H	Select connected copper
CTRL + SHIFT + Left-click & hold	Break track
SHIFT + CTRL + Left-click	Highlight additional routed net under cursor
+ (numeric keypad)	Next layer
- (numeric keypad)	Previous layer
CTRL + Click	Highlights layer content on layer tabs
CTRL + SHIFT + Click	Increments highlighting on layer tabs
CTRL + ALT + Mouse	Hovers highlight layer on layer tabs
* (numeric keypad)	Next routing layer
M	Display Move sub-menu
ALT	Hold to temporarily switch from avoid-obstacle to ignore-obstacle mode
CTRL	Hold to temporarily disable electrical grid while routing
CTRL + M	Measure distance
SPACEBAR (in interactive process)	Rotate object anti-clockwise (define rotation step on PCB Editor - General page of Preferences dialog)
SPACEBAR (during interactive routing)	Toggle start/end mode
SHIFT + SPACEBAR (in interactive process)	Rotate object being moved clockwise
SHIFT + SPACEBAR (during interactive routing)	Step through corner modes during interactive routing
[	Decrease mask level for permanent filter
]	Increase mask level for permanent filter
ALT ←	View previous component for active library document
ALT →	View next component for active library document
Q	Toggle units (metric/imperial)
Ctrl + Q	Toggle units (metric/imperial) within an open PCB Editor dialog
T, B	Access 3D Body Manager dialog
T, P	Access Preferences dialog
BACKSPACE	Remove last interactive length tuning segment
SPACEBAR	Next interactive length tuning wave pattern
SHIFT + SPACEBAR	Previous interactive length tuning tuning pattern
SHIFT + R	Toggle Routing Mode
, (comma)	Decrease interactive length tuning pattern amplitude by one increment
. (full stop / period)	Increase interactive length tuning pattern amplitude by one increment
1	Decrease interactive length tuning miter or radius
2	Increase interactive length tuning miter or radius
3	Decrease interactive length tuning pattern gap by increment
4	Increase interactive length tuning pattern gap by increment
Y	Toggle interactive length tuning amplitude direction

### Interactive Routing Shortcuts
Shift+F1 (or ~ (tilde))	Display list of shortcuts
CTRL + Click	Auto-complete segments to target
BACKSPACE	Remove last segment
ESC	Terminate current trace
SHIFT + A	Add accordion sections (interactive length tuning)
SHIFT + C	Toggle auto-complete
SHIFT + G	Toggle length tuning gauge
SHIFT + O	Toggle visible routing area
SHIFT + P	Toggle Push mode
SHIFT + Q	Toggle glossing
SHIFT + R	Toggle routing mode
SHIFT + S	Switch layer for current trace
SHIFT + V	Select favorite via size
SHIFT + W	Open Choose Favorite Width dialog.
, (comma)	Decrease arc setback
SHIFT + . (comma)	Decrease arc setback 10x
. (full stop / period)	Increase arc setback
SHIFT + . (full stop / period)	Increase arc setback 10x
ENTER	Place Segment
+ (plus)	Next Layer (numeric keypad)
- (minus)	Previous Layer (numeric keypad)
* (multiply)	Next Signal Layer (numeric keypad)
SPACEBAR	Cycle corner direction
SHIFT + SPACEBAR	Cycle corner styles (if restrict to 90/45° is not enabled)
TAB	Edit trace properties
1	Toggle Look-ahead Mode – Switches between 1 and 2 segment placement mode
2	Add via, no layer change
SHIFT + 2	Add fanout via, tool immediately waits for next fanout to route and via to place
3	Cycle track width source
4	Cycle via size source
6	Force walk-around (with key pressed)
7	Switch leader trace or switch routing target in single trace mode
8	Toggle dynamic routing mode
9	Switches to opposite routing point

### Interactive Differential Pair Routing Shortcuts
Shift+F1 (or ~ (tilde))	Display list of shortcuts
CTRL + Click	Commit auto complete segments (if applicable)
BACKSPACE	Remove last segment
SHIFT + BACKSPACE	Remove last cluster of segments
ESC	Terminate current trace
SHIFT + R	Toggle routing mode
SHIFT + W	Open Choose Favorite Width dialog.
ENTER	Place segment
+ (plus)	Next layer
- (minus)	Previous layer
* (multiply)	Next signal layer
SPACEBAR	Toggle corner direction
SHIFT + SPACEBAR	Cycle corner styles (if restrict to 90/45° is not enabled)
TAB	Edit trace properties
3	Cycle track width source
4	Cycle via size source
5	Toggle Auto-complete
6	Change via mode

### Interactive Length Tuning Shortcuts
Shift+F1 (or ~ (tilde))	Display list of shortcuts
TAB	Edit tuning pattern settings
BACKSPACE	Remove last segment
SPACEBAR	Next tuning pattern
SHIFT + SPACEBAR	Previous tuning pattern
SHIFT + R	Toggle Routing Mode
, (comma)	Decrease pattern amplitude by one increment
. (full stop / period)	Increase pattern amplitude by one increment
1	Decrease miter or radius
2	Increase miter or radius
3	Decrease pattern gap by increment
4	Increase pattern gap by increment
Y	Toggle amplitude direction

Efc verander referentie
fl zet center op locatie